Work Insturction for 24171BBA01 Cutter Bearing

Modified Item: 625ZZ (16 mm OD,5 mm ID, 5 mm high shielded) roller bearing.

WARNING
Eye hazard. Bearing or grinder could come apart at any moment while rotating around 10,000 RPM.

1. Install grinding bit with flat face in spindle. Aluminum oxide or ceramic aluminum oxide preferred.
2. Mount on CNC table into M5 threaded hole assembled in the following order, bottom to top:
  1. standoff with 5 mm through hole ID (if necessary)
  2. M5 washer
  3. Bearing
  4. M5 socket cap screw
3. Tighten screw until bearing resists spinning. Loosen just until bearing is able to spin freely.
4. Zero spindle at point where outer edge of grinder is 2 mm inside bearing outer edge and is bottom of grinder is just touching bearing.
5. Start spindle and move downward by 0.01 mm steps until contact is made and bearing spins freely.
6. Grind downward by 0.01 or 0.02 mm steps until chamfer is removed from bearing, about 0.4 mm. Check removal of chamfer with fingernail: bearing should shave nail when nail is scraped along bearing almost parallel to circumference.
7. For final grind, grind without moving downward until contact between grinder and bearing is lost.