Work Insturction for 24171BBA02 Pultrusion Nozzle

Modified Item: Ender 3 compatible brass nozzle (6 mm hex nut, M6 thread, any nozzle diameter).

Equipment Required
- Drill press
- M6 hex socket
- 1.8? mm drill bit
- 1.7 mm drill bit
- 1/16” or 1 mm tapered router bit
- Old header block

1. Install 1.8 drill bit in drill press
2. Clamp hex socket onto drill press table
3. Insert nozzle tip down into hex socket
4. Center nozzle under 1.8 mm bit
5. Replace bit with 1.7 mm bit
6. Drill through nozzle
7. Replace bit with tapered bit
8. Taper hole as much as possible without damaging threads
9. Remove nozzle and thread into heater block
10. Clamp heater block into vice and file tip of nozzle flat
11. Remove burrs with steel dwire brush