Work Instruction for 24180BBABS PET Bottle Cutter
# Assembled Item
Bill of Materials
Reference Letter	Quantity	Part Number	Description
A	2		Mounting plate
B	1		Bottle support
C	2		5M x ?? screw
D	2		bearing
E	1		Spring
F	1		Set Screw
G

Equipment Required
- 4 mm hex wrench
- 2.5 mm hex wrench

1. Verify Bottle Support (B) fits in Mounting Plate (A). Drill with 9 mm (23/64 in, 0.36 in) bit if necessary.
2. Place Bearing (D), then Spring (E) on Screw (C).
3. Using hex wrench, screw Screw (C) into bottom center hole on Mounting Plate (A) until bearing is just below the top of the bottle guide.
4. Place the other Bearing (D) on the other Screw ©.
5. Using hex wrench, screw Screw (C) into top center hole on Mounting Plate (A) until it stops.
6. Loosen the first screw until the two bearing turn tightly together.
7. Screw the Set Screw (F) into the center of the Bottle Guide until the top is around the forth mark from the top.